## Slide 1
EdgeAI TensorLab
Training, Optimizing & Deploying Deep Learning Models on TI Edge AI Processors
Publisher: Texas Instruments Incorporated
Toolkit: github.com/TexasInstruments/edgeai-tensorlab
Target: TDA4VM | AM68A | AM69A | AM62A
Edge AI | Quantization | ONNX | TIDL
TRAIN
QUANTIZE
EXPORT
DEPLOY

## Slide 2
Presentation Overview
What we will cover across these 22 slides
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 2 / 22
01
Introduction & Hardware Ecosystem
What EdgeAI TensorLab is, and the TI processor families it targets
02
Architecture & Model Zoo
Repository structure, 300+ pre-trained models, and supported tasks
03
Model Training
Classification, detection, and segmentation training frameworks
04
Optimization Toolkit
Layer surgery, structured pruning, and hardware-aware design
05
Quantization & Deployment
QAT, PTQ, ONNX export, TIDL compilation, and real hardware results

## Slide 3
What is EdgeAI TensorLab?
An open-source toolkit by Texas Instruments for end-to-end deep learning at the edge
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 3 / 22
EdgeAI TensorLab is TI's comprehensive open-source toolkit that enables engineers to train, optimize, quantize, and deploy deep learning models directly onto TI edge AI processors — with accuracy preserved and latency minimized.
01 Train
PyTorch-based training for classification, detection, segmentation, and pose estimation. Integrates with mmdetection and mmsegmentation.
02 Optimize
Layer surgery, structured pruning, and hardware-aware architecture design to maximize efficiency on TI silicon.
03 Quantize
8-bit Quantization-Aware Training (QAT) and Post-Training Quantization (PTQ) with power-of-2 scale constraints for TIDL compatibility.
04 Deploy
ONNX and TFLite export, TIDL compiler integration, and device-specific optimization for TDA4VM, AM68A, AM69A, and AM62A processors.

## Slide 4
TI Edge AI Hardware Ecosystem
Processor families supported by EdgeAI TensorLab
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 4 / 22
AUTOMOTIVE & INDUSTRIAL PROCESSORS
TDA4VM / J7x
Automotive ADAS & AD
▸ 8 TOPS MMA accelerator
▸ 4× ARM Cortex-A72 cores
▸ ISO 26262 functional safety
▸ Primary TensorLab target
AM68A
Industrial & Automotive
▸ 4 TOPS MMA accelerator
▸ 2× ARM Cortex-A53 cores
▸ IEC 61508 safety rating
▸ Cameras + display support
AM69A
High-Performance Multi-Camera
▸ 32 TOPS MMA accelerator
▸ 8× ARM Cortex-A72 cores
▸ ISO 26262 functional safety
▸ Multi-sensor fusion capable
AM62A
Ultra-Low Power IoT / Edge
▸ 1 TOP MMA accelerator
▸ ARM Cortex-A53 core
▸ Sub-2W power envelope
▸ Industrial IoT deployments
EVALUATION BOARDS
SK-TDA4VM
Starter kit — cameras, displays, full dev environment
AM68A-SK
Industrial evaluation — USB, Ethernet, PCIe interfaces
BeagleBone AI-64
Community board — TDA4VM-based, open ecosystem

## Slide 5
Repository Architecture
Six interconnected sub-repositories forming the complete toolkit
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 5 / 22
EdgeAI TensorLab uses a modular design — each sub-repository handles one part of the ML lifecycle. They are independently usable and deeply interconnected.
edgeai-torchvision
Extended PyTorch vision library. Adds TI-specific model variants, quantization-aware layers, and hardware-friendly operators.
edgeai-modelzoo
Collection of 300+ pre-trained models. Every model is validated for TIDL compatibility and benchmarked on TI hardware.
edgeai-modeloptimization
Quantization (QAT/PTQ), structured pruning, and layer surgery tools. Core toolkit for reducing model size and improving latency.
edgeai-mmdetection
TI-adapted mmdetection framework. Trains YOLOX, SSD, RetinaNet, FCOS, and more with TIDL-compatible configurations.
edgeai-mmsegmentation
TI-adapted mmsegmentation framework. Trains DeepLabV3+, FastSCNN, DDRNet, and HRNet for semantic segmentation.
edgeai-benchmark
Accuracy and performance benchmarking suite. Measures Top-1/mAP/mIoU, latency, FPS, model size, and memory footprint.

## Slide 6
Model Zoo — 300+ Pre-Trained Models
TIDL-validated, benchmarked, and deployment-ready
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 6 / 22
300+
Pre-trained models
6+
Supported task types
8-bit
INT8 quantized ready
100%
TIDL compatible
MODEL FAMILIES
Classification
▸ MobileNetV1 / V2 / V3
▸ EfficientNet-Lite 0–4
▸ ResNet 18 / 50
▸ ShuffleNetV2
▸ GhostNet / RegNet
▸ ViT & DeiT (lite)
Object Detection
▸ YOLOX-nano / tiny / small
▸ SSD-MobileNet variants
▸ RetinaNet / FCOS
▸ EfficientDet
▸ CenterNet
▸ NanoDet
Segmentation
▸ DeepLabV3+ (MBV2/V3)
▸ FastSCNN
▸ DDRNet-23 / 39
▸ HRNet / LiteHRNet
▸ BiSeNetV1 / V2
▸ SegFormer (lite)
Other Tasks
▸ HRNet — Pose Estimation
▸ LiteHRNet — Lightweight Pose
▸ RetinaFace — Face Detection
▸ SCRFD — Face Detection
▸ DepthAnything Lite
▸ DORN — Depth Estimation

## Slide 7
Model Naming Convention & Selection
How to read and choose the right model from the Model Zoo
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 7 / 22
NAMING CONVENTION DECODED
Every model name encodes its architecture, source, scale, training method, and quantization properties — making selection fast and unambiguous.
mobilenet_v2
Base architecture
_tv_
Source (torchvision)
x1
Width multiplier (1.0×)
_qat
Quantization-Aware Trained
-p2
Power-of-2 scales
.onnx
Export format
HOW TO CHOOSE THE RIGHT MODEL
Latency is the priority
Choose MobileNetV2 x0.5 or x0.75, EfficientNet-Lite0, FastSCNN, or YOLOX-nano variants
Accuracy is the priority
Choose EfficientNet-Lite4, ResNet50, YOLOX-small, or DeepLabV3+ with a wider backbone
Smallest possible model
Choose GhostNet, ShuffleNetV2, NanoDet, or LiteHRNet with reduced width
Production deployment
Always use a _qat-p2 (Quantization-Aware Trained, Power-of-2) variant for best INT8 accuracy

## Slide 8
Supported AI Tasks
Six task categories, each with dedicated models and training frameworks
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 8 / 22
Image Classification
What is in this image?
ImageNet 1000 classes
▸ MobileNet, EfficientNet-Lite
▸ ResNet, GhostNet, RegNet
▸ Top-1 accuracy metric
▸ Fastest inference task
Object Detection
Where are the objects?
COCO 80 classes
▸ YOLOX, SSD, RetinaNet
▸ FCOS, EfficientDet
▸ mAP@0.5 metric
▸ Bounding box predictions
Semantic Segmentation
Label every single pixel
Cityscapes 19 classes
▸ DeepLabV3+, FastSCNN
▸ DDRNet, HRNet
▸ mIoU metric
▸ Per-pixel classification
Pose Estimation
Locate human body joints
COCO Keypoints
▸ HRNet, LiteHRNet
▸ 17 keypoints per person
▸ OKS metric
▸ Real-time capable
Depth Estimation
How far away is each pixel?
KITTI / NYU Depth
▸ DepthAnything Lite
▸ DORN architecture
▸ Absolute Rel. metric
▸ Monocular input
Face Detection
Detect and localize faces
WiderFace benchmark
▸ RetinaFace, SCRFD
▸ AP metric across scales
▸ Multi-scale detection
▸ Landmark localization

## Slide 9
Model Training Framework
Three PyTorch-based frameworks covering all supported tasks
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 9 / 22
TensorLab integrates three established PyTorch frameworks, each extended with TI-specific configurations, hardware-friendly default settings, and TIDL-compatible model variants.
edgeai-torchvision
Classification & Detection
▸ Extended PyTorch torchvision library
▸ TI-optimized MobileNet, EfficientNet, ResNet
▸ SSD and related detection architectures
▸ ImageNet training reference scripts included
▸ Transfer learning and fine-tuning support
edgeai-mmdetection
Advanced Object Detection
▸ YOLOX, RetinaNet, FCOS, Faster RCNN
▸ YAML config system — modify without code changes
▸ Mosaic and MixUp augmentation pipelines
▸ Multi-GPU distributed training ready
▸ COCO evaluation metrics built-in
edgeai-mmsegmentation
Semantic Segmentation
▸ DeepLabV3+, FastSCNN, DDRNet, HRNet
▸ Cityscapes and ADE20K dataset support
▸ Multi-scale inference for best mIoU
▸ Lightweight backbone swap in config
▸ Panoptic segmentation variants available

## Slide 10
Training Best Practices
TI-recommended settings for accuracy, stability, and deployment readiness
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 10 / 22
ARCHITECTURE RULES
TRAINING RECIPE
▸ Use ReLU or ReLU6 activations only — not SiLU, GELU, Mish, or Hardswish
▸ Prefer depthwise separable convolutions for lower compute and TIDL efficiency
▸ Use static input shapes — dynamic shapes prevent correct ONNX export
▸ Verify all operators appear in the TIDL supported operator list before training
▸ Avoid Python control flow inside exported model forward pass
▸ Cosine annealing LR scheduler with 5-epoch linear warmup
▸ Label smoothing at 0.1 — reduces overconfidence
▸ MixUp (alpha=0.2) and CutMix (alpha=1.0) data augmentation
▸ Exponential Moving Average (EMA) of weights for best checkpoint
▸ Gradient clipping at max_norm=1.0 for training stability
TRANSFER LEARNING WORKFLOW
Step 1
Load ImageNet-pretrained TI model
→
Step 2
Freeze feature extractor layers
→
Step 3
Replace and train classifier head
→
Step 4
Gradually unfreeze all layers
→
Step 5
Fine-tune at 10× lower learning rate

## Slide 11
Why Optimization is Non-Negotiable
The gap between a research model and a deployable model
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 11 / 22
UNOPTIMIZED
OPTIMIZED
ResNet50 (Float32, unmodified)
📦 Model size: 97 MB
⏱ Latency: 580 ms on TDA4VM
⚡ Throughput: ~1.7 FPS
🔋 Power: 3.2 W
❌ Cannot meet real-time requirements
VS
MobileNetV2 (INT8 QAT, optimized)
📦 Model size: 4.1 MB
⏱ Latency: 2.3 ms on TDA4VM
⚡ Throughput: 435 FPS
🔋 Power: 0.8 W
✅ Production-ready real-time inference
24× Smaller Model | 252× Faster Latency | 4× Lower Power | <1% Accuracy Loss
KEY INSIGHT
Optimization is not an afterthought — it is an integral part of the design process. TensorLab's toolkit makes it systematic, measurable, and reproducible.

## Slide 12
Three Pillars of Model Optimization
Sequential techniques for maximum efficiency on TI hardware
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 12 / 22
PILLAR 1
Layer Surgery
Replace hardware-incompatible operators before training
▸ SiLU / GELU / Mish → ReLU
▸ Hardswish → ReLU6
▸ Non-standard SE blocks → lite variants
▸ No accuracy loss — equivalent math
▸ Required before TIDL compilation
PILLAR 2
Structured Pruning
Remove redundant weights and channels
▸ Target 30–50% weight reduction
▸ Iterative: prune → fine-tune → repeat
▸ L1-norm channel pruning (structured)
▸ Minimal accuracy impact if done gradually
▸ Requires retraining after pruning
PILLAR 3
Quantization
Reduce from 32-bit float to 8-bit integer
▸ 4× model size reduction
▸ 2–4× inference speedup on MMA
▸ Requires power-of-2 scale constraint
▸ Two paths: QAT or PTQ
▸ <1% accuracy loss achievable
Apply in order: Surgery first → Pruning second → Quantization last — each step builds on the previous.

## Slide 13
Quantization — Making Models Hardware-Friendly
The most impactful single optimization for TI edge deployment
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 13 / 22
Quantization converts 32-bit floating-point weights and activations into 8-bit integers — reducing model size 4× and enabling the TI MMA (Matrix Multiply Accelerator) to run at full hardware throughput.
WHAT IS QUANTIZED
Weights
Per-channel INT8 — best accuracy
Activations
Per-tensor INT8 — hardware efficient
Biases
INT32 — kept at higher precision
BN Stats
Folded into conv — zero overhead
TI HARDWARE REQUIREMENTS
⚠ CRITICAL — Power-of-2 Scales TI hardware requires quantization scale factors to be exact powers of 2 (1, 2, 4, 8, 16 …). This must be enabled in the quantization config. Floating-point scales will fail at TIDL compile time.
▸ Symmetric weight quantization
▸ Unsigned activations after ReLU layers
▸ Per-channel quantization for weights
▸ Per-tensor quantization for activations
▸ Batch Norm folded into convolution
▸ ONNX opset 11 for TIDL compiler
BENEFITS ON TI HARDWARE
4×
Model Size
2–4×
Inference Speed
75%
Memory Bandwidth
<1%
Accuracy Loss

## Slide 14
QAT vs PTQ — Choosing Your Strategy
Two paths to INT8 — tradeoffs explained
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 14 / 22
Criteria
Post-Training Quant (PTQ)
Quantization-Aware Training (QAT)
Retraining Required
❌ No retraining needed
✅ 10–20 fine-tuning epochs
Calibration Data
100–1000 representative samples
Full training dataset
Time to Complete
⚡ Minutes to hours
⏱ Hours to days
Typical Accuracy Loss
1–3% below float baseline
<1% below float baseline ✓
Best Use Case
Quick prototyping & validation
Production deployment
Complexity
Low — minimal setup
Medium — training loop required
TI Recommendation
Good starting point
✅✅ Preferred for release
QAT Workflow: Float Training → Insert Fake-Quant Nodes → Fine-tune 10–20 epochs at 10× lower LR → Freeze BN stats at epoch 5 → Convert to INT8 → ONNX Export → TIDL Compile

## Slide 15
QAT Training Workflow
Step-by-step process for production-quality INT8 models
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 15 / 22
STEP 1
Start from Trained Float Model
Load a converged Float32 checkpoint — do not start QAT from scratch. QAT is fine-tuning, not training from zero.
STEP 2
Configure Quantization Settings
Enable power-of-2 scales, per-channel weight quantization, symmetric weights, and unsigned activations in the config file.
STEP 3
Fine-Tune with Fake-Quantization
Train for 10–20 epochs at 1/10th the original learning rate. Fake-quant nodes simulate INT8 rounding during forward pass.
STEP 4
Freeze Batch Norm Statistics
After epoch 5, freeze BN running stats. This stabilizes quantization scale estimation and prevents drift.
STEP 5
Validate Accuracy — Check the Drop
Run full validation. Acceptable: <1% accuracy loss. If >2% loss, revisit LR, epoch count, or observer settings.
STEP 6
Convert to INT8 and Export
Convert model to fully quantized INT8. Export to ONNX opset 11. Run onnx-simplifier. Deploy to TI hardware.

## Slide 16
ONNX Export — The Bridge to Hardware
Exporting models correctly for TIDL compilation
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 16 / 22
ONNX (Open Neural Network Exchange) is the standard interchange format used by TI TIDL. A correctly exported and simplified ONNX model is required before any TI hardware compilation can begin.
EXPORT PIPELINE
QAT Model (.pth)
→
torch.onnx .export()
→
Raw ONNX Graph
→
onnx-sim simplify
→
TIDL-ready ONNX
EXPORT REQUIREMENTS
▸ Opset version 11 — TI TIDL requirement
▸ Static input shapes — no dynamic axes in model
▸ Set input_names and output_names explicitly
▸ Enable do_constant_folding for smaller graph
▸ Run onnx-simplifier after export
▸ Validate ONNX vs PyTorch output numerically
TIDL OPERATOR SUPPORT
✅
Conv2d (3×3, 1×1, 5×5, 7×7)
✅
DepthwiseConv2d — all strides
✅
BatchNorm — fused with Conv
✅
ReLU / ReLU6 | MaxPool / AvgPool
✅
Add / Concat / Multiply / GlobalAvgPool
✅
Upsample — bilinear & nearest
⚠️
GroupConv — ARM fallback only
❌
Custom CUDA kernels — not supported

## Slide 17
Benchmarking & Evaluation
Measuring what matters — accuracy, latency, and efficiency
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 18 / 22
Accuracy
▸ Top-1 / Top-5 (classification)
▸ mAP@0.5:0.95 (detection)
▸ mIoU (segmentation)
▸ OKS (pose estimation)
Latency
▸ Mean / P50 / P95 / P99
▸ ms per frame
▸ FPS throughput
▸ Warm-up vs sustained
Model Size
▸ MB on disk
▸ Parameter count
▸ MACs / GFLOPs
▸ Compression ratio
Memory
▸ Peak GPU / SRAM usage
▸ DDR bandwidth
▸ Activation memory
▸ Runtime overhead
EVALUATION TOOLS
edgeai-benchmark
Full accuracy + latency suite. Runs classification, detection, and segmentation benchmarks with a single command.
TensorBoard
Training curve visualization. Loss, accuracy, LR, and weight histograms updated in real-time during training.
COCO eval / Cityscapes eval
Standard benchmark evaluation scripts. Produces official mAP and mIoU numbers comparable to published papers.
Layer Profiler
Per-layer latency breakdown on TI hardware. Identifies bottlenecks for targeted architectural improvements.

## Slide 18
Real-World Performance on TDA4VM
Measured on SK-TDA4VM Evaluation Board (8 TOPS MMA)
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge
Slide 19 / 22
All numbers measured with INT8 QAT models compiled by TIDL. Latency = end-to-end inference including pre/post processing. Accuracy = validation set, standard benchmarks.
Model
Task
Accuracy
Latency
Size
MobileNetV2 x1.0
Classification
71.8% Top-1
2.3 ms
3.4 MB
EfficientNet-Lite0
Classification
75.1% Top-1
3.1 ms
4.7 MB
ResNet18
Classification
69.7% Top-1
4.2 ms
44 MB
YOLOX-tiny
Detection
32.8 mAP
8.5 ms
5.0 MB
SSD-MobileNetV2
Detection
22.1 mAP
6.7 ms
16 MB
DeepLabV3+-MBV2
Segmentation
73.2 mIoU
15.2 ms
8.3 MB
FastSCNN
Segmentation
70.8 mIoU
8.9 ms
1.1 MB
Key takeaway: FastSCNN achieves 70.8 mIoU segmentation at only 1.1 MB — a direct result of hardware-aware architecture + INT8 QAT optimization. Always validate on actual TI silicon — GPU benchmarks do not predict edge performance.

## Slide 19
Thank You
GitHub Repository:
github.com/TexasInstruments/edgeai-tensorlab
Toolkit:
EdgeAI TensorLab
Publisher:
Texas Instruments Incorporated
Target HW:
TDA4VM / AM68A / AM69A
License:
Apache 2.0 — Open Source
Framework:
PyTorch + ONNX + TIDL
Texas Instruments | EdgeAI TensorLab | Deep Learning for the Edge